FCC labelling and user Information

All devices subject to the authorization procedure Certification are required to display an identification label/plate showing the FCC Identifier (FCC ID under which they are authorized). See section 2.925 and 2.926 for detailed identification requirements. Additional labeling requirements may be specified in the FCC Rules (in particular see 15.19) governing the particular class of equipment.

Section 2.925 (a) Each equipment covered in an application for equipment authorization shall bear a nameplate or label listing the following: (1) FCC Identifier consisting of the two elements in the exact order specified in Section 2.926. The FCC Identifier shall be preceded by the term FCC ID in capital letters on a single line, and shall be of a type size large enough to be legible without the aid of magnification:

Section 2.926 (d) The equipment product code assigned by the grantee shall consist of a series of Arabic numerals, capital letters or a combination thereof, and may include the dash or hyphen (-). The total of Arabic numerals, capital letters and dashes or hyphens shall not exceed 14 and shall be one which has not been previously used in conjunction with: (1) The same grantee code, or (2) An application denied pursuant to 2.919 of this chapter

The FCC ID consists of two elements, a Grantee code and an equipment product code (EPC).

Example for FCC ID:

FCC ID AAAXXXXX

AAA = 3 character Grantee code assigned permanently by the FCC to a specific grantee and is valid only for the party listed, and at the address listed in the Notification of Code Assignment

XXXXX = Equipment product code (EPC) assigned by the applicant. Minimum of 1 character and maximum of 14 characters and may consist

ONLY of capital letters, Arabic numerals or combination thereof, the hyphen or dash (-). Applicant should assign the least number of characters that will adequately identify the product.

Note:

Section 2.925 (d) In order to validate the grant of equipment authorization, the nameplate or label shall be permanently affixed to the equipment and shall be readily visible to the purchaser at the time of purchase.

- As used here, permanently affixed means that the required nameplate data is etched, engraved, stamped, indelibly printed, or otherwise permanently marked on a permanently attached part of the equipment enclosure. Alternatively, the required information may be permanently marked on a nameplate of metal, plastic, or other material fastened to the equipment enclosure by welding, riveting, etc., or with a permanent adhesive. Such a nameplate must be able to last the expected lifetime of the equipment in the environment in which the equipment will be operated and must not be readily detachable.

- As used here, readily visible means that the nameplate or nameplate data must be visible from the outside of the equipment enclosure. It is preferable that it be visible at all times during normal installation or use, but this is not a prerequisite for grant of equipment authorization.